..HEAD01L 1994 CORPORATE SENSING AND DIAGNOSTIC MODULE - SDM

..FOOT63R A252  PAGE ##

DATA STREAM A252  SPECIFICATION

..PAGE

SPECIFICATIONS FOR DATA STREAM INFORMATION

------------------------------------------

CORPORATE SENSING AND DIAGNOSTIC MODULE (SDM)

USAGE:   1994        1,4B 6D 1,2W  CAR

*           1995        2,3,4H 3,4C 1,4B 6D 1W CAR

DATA PIN: READ DATA ON PIN "M" OF ALDL CONNECTOR

BAUD RATE: 8192

..PAGE

MODE 1  (TRANSMIT FIXED DATA STREAM MESSAGE 0)

ALDL REQUEST:

- MESSAGE ID            = $FA

- MESSAGE LENGTH        = $57

- MODE NUMBER           = $01

- MESSAGE NUMBER        = $00

- CHECKSUM

THE SDM WILL RESPOND WITH THE FOLLOWING MESSAGE:

- MESSAGE ID            = $FA

- MESSAGE LENGTH        = $72

- MODE NUMBER           = $01

- MESSAGE NUMBER        = $00

- DATA BYTE 1

.

.

- DATA BYTE 27

- CHECKSUM

MODE 10 (CLEAR MALFUNCTION CODES - TESTER TO SDM)

ALDL REQUEST:

- MESSAGE ID            = $FA

- MESSAGE LENGTH        = $56

- MODE NUMBER           = $0A

- CHECKSUM

THE SDM WILL RESPOND WITH THE FOLLOWING MESSAGE:

- MESSAGE ID            = $FA

- MESSAGE LENGTH        = $56

- MODE NUMBER           = $0A

- CHECKSUM

..PAGE

..HEAD02L ALDL DATA LIST

..HEAD03L NUMBER OF DATA WORDS - 27

..HEAD04L ALDL MODE 1 DATA LIST MESSAGE 0

WORD    DESCRIPTION

1      IGNITION

VOLTS = N/12.25

2      SENSELO

VOLTS = N/6.375

3      36VLR

VOLTS = N/6.0714

4      DRIVER VDIF

mV = N/.255

5      PASS. VDIF

mV = N/.255

6      NOT USED

7      NOT USED

8      NOT USED

9      DRIVER RESIST.

OHMS = N/10

10     PASS. RESIST.

OHMS = N/10

11     DISCRETE STATUS

7   NOT USED

6   NOT USED

5   LAMP DRIVER                            1 = EXTERNAL   0 = INTERNAL

4   DRIVER SEATBELT                        1 = BUCKLED    0 = UNBUCKLED

3   NOT USED

2   NOT USED

1   NOT USED

0   NOT USED

12     ACTIVE FAULT CODE WORD 1

7   FAULT CODE 15

6   FAULT CODE 16

5   FAULT CODE 17

4   FAULT CODE 21

3   FAULT CODE 22

2   FAULT CODE 24

1   FAULT CODE 25

0   FAULT CODE 26

13     ACTIVE FAULT CODE WORD 2

7   FAULT CODE 35

6   FAULT CODE 36

5   FAULT CODE 37

4   FAULT CODE 38

3   FAULT CODE 51

2   FAULT CODE 52

1   FAULT CODE 55

0   FAULT CODE 61

..page

14     ACTIVE FAULT CODE WORD 3

7   FAULT CODE 62

6   FAULT CODE 71

5   NOT USED

4   NOT USED

3   NOT USED

2   NOT USED

1   NOT USED

0   NOT USED

15     HISTORY FAULT CODE WORD 1

7   FAULT CODE 15

6   FAULT CODE 16

5   FAULT CODE 17

4   FAULT CODE 21

3   FAULT CODE 22

2   FAULT CODE 24

1   FAULT CODE 25

0   FAULT CODE 26

16     HISTORY FAULT CODE WORD 2

7   FAULT CODE 35

6   FAULT CODE 36

5   FAULT CODE 37

4   FAULT CODE 38

3   FAULT CODE 51

2   FAULT CODE 52

1   FAULT CODE 55

0   FAULT CODE 61

17     HISTORY FAULT CODE WORD 3

7   FAULT CODE 62

6   FAULT CODE 71

5   NOT USED

4   NOT USED

3   NOT USED

2   NOT USED

1   NOT USED

0   NOT USED

18     NOT USED

19     NOT USED

20     ROM IDENTIFICATION

ID = N

21     DISCRETE STATUS

7   ARMING SENSOR                          1 = OVERLAP    0 = NO OVERLAP

6   NOT USED

5   NOT USED

4   NOT USED

3   NOT USED

2   NOT USED

1   ADS*                                   1 = NOT CLOSED 0 = CLOSED

0   NOT USED

..page

22     DISCR

7   NOT USED

6   NOT USED

5   BACKUP WARNING                         1 = ACTIVE     0 = INACTIVE

4   NOT USED

3   36VEN                                  1 = ACTIVE     0 = INACTIVE

2   NOT USED

1   NOT USED

0   NOT USED

23     DISCRETE STATUS

7   NOT USED

6   1ST LAMP DRIVER                        1 = ACTIVE     0 = INACTIVE

5   2ND LAMP DRIVER                        1 = ACTIVE     0 = INACTIVE

4   NOT USED

3   NOT USED

2   CRANK                                  1 = ACTIVE     0 = INACTIVE

1   NOT USED

0   NOT USED                                                            T

24     NOT USED

25     VEHICLE ID

ID = N

26     PLATFORM ID

ID = N

27     CAL LEVEL

LEVEL = N