DATA STREAM  A1
            1.8l TBI   (LH8)   (VIN=0)   82, 83, 84, 85, 86
            2.0l TBI   (LQ5)   (VIN=P)   83
            2.5l TBI   (LR8)   (VIN=R)   83, 84, 85, 86
            2.5l TBI   (L68)   (VIN=U)   83, 84, 85, 86
            2.5l TBI   (LN8)   (VIN=E)   85, 86  TRUCKS
            2.5l TBI   (LQ9)   (VIN=2)   83, 84, 85, 86
            5.0  CFI   (LU5)   (VIN=S)   83


  DATA STREAM  A2
            3.8l MFI   (LN3)   (VIN=3)   84


  DATA STREAM
            3.8l  SFI  (LG3)   (VIN=3)   86  (A/H CARS)
            3.8l  SFI  (LG2)   (VIN=B)   86  (A/H CARS)
            3.8l  SFI  (LC2)   (VIN=7)   86  (G CARS)


  DATA STREAM  A4
            3.8l  SFI  (LG2)    (VIN=b)  86  'Buick E' Only


  DATA STREAM  A5
            3.0   CLCC (LK9)   (VIN=E)   84  85         (84)
            3.8l  CLCC (LD5)   (VIN=A)   84, 85, 86, 87 (87)
            4.1l  CLCC (LC4)   (VIN=4)   84, 85
            4.3L  CLCC (LS5)   (VIN=S)   85, 86


  DATA STREAM  A6
            5.0l  CLCC (LV2)   (VIN=Y)   84
            5.0l  CLCC (L69)   (VIN=G)   84
            5.0l  CLCC (LG4)   (VIN=H)   84
            5.0l  CLCC (LG8)   (VIN=9)   84
            5.7l  CLCC (LM1)   (VIN=6)   84


  DATA STREAM  A7
            5.0l  CLCC (LV2)   (VIN=Y)   85, 86, 87
            5.0l  CLCC (LG8)   (VIN=9)   85
            5.0l  CLCC (L69)   (VIN=G)   85, 86, 87, 88
            5.0L  CLCC (LG4)   (VIN=H)   85, 86, 87
            5.7L  CLCC (LM1)   (VIN=6)   85, 86, 87, 88
            4.3L  CLCC (LB1)   (VIN=N)   85, 86
            5.0L  CLCC (LF3)   (VIN=H)   85, 86
            5.7L  CLCC (LS9)   (VIN=L)   85, 86


  DATA STREAM  A8
            3.8l  SFI  (LG3)   (VIN=3)   86  (A/C/H CARS)
            3.8l  SFI  (LC2)   (VIN=7)   86  (G CARS)
            3.8l  SFI  (LG2)   (VIN=B)   86  (A/C/H CARS)
            3.8l  SFI  (LG3)   (VIN=3)   87, 88
            3.8l  SFI  (LG2)   (VIN=B)   86, 87
            3.8l  SFI  (LC2)   (VIN=7)   87, 89, 91


  DATA STREAM A10
            3.0l  MFI  (LN7)   (VIN=L)   86  (H/N CARS)


  DATA STREAM A11
            3.0l  MFI  (LN7)   (VIN=L)   86  (H/N CARS)
            3.0l  MFI  (LN7)   (VIN=L)   87, 88


  DATA STREAM A12
            3.8l  CLC  (LC3)   (VIN=9)   84


  DATA STREAM A14
            3.0l MFI   (LN7)   (VIN=L)   85
            3.8l MFI   (LN3)   (VIN=3)   85
            3.8l SFI-T(LM9)    (VIN=9)   84, 85


  DATA STREAM A15
            1.8l MFI-T (LA5)   (VIN=J)   84, 85


  DATA STREAM A16
            1.8l MFI-T (LA5)   (VIN=J)   86

  DATA STREAM A17
            2.0l TBI   (LQ5)   (VIN=P)    84, 85, 86
            2.5l TBI   (LR8)   (VIN=R)    82


  DATA STREAM A18
             2.8 CARB   (LE2)   (VIN=X)   84, 85
             2.8 CARB   (LC1)   (VIN=1)   84
             2.8 CARB   (LH7)   (VIN=Z)   84
             2.8 CARB   (LL1)   (VIN=L)   84
             2.8 CARB   (LR2)   (VIN=B)   84, 85


  DATA STREAM A19
            2.8l CARB  (LE2)   (VIN=X)    86


  DATA STREAM A20
            2.8l MFI   (LB6)   (VIN=W)   85, 86
            2.8l MFI   (LB8)   (VIN=S)   86, 87, 88, 89
            5.0l MFI   (LB9)   (VIN=F)   85


  DATA STREAM A21
            4.1l DFI   (LT8)   (VIN=8)   85 CADILLAC "C" CAR


             DATA STREAM A22
                   4.1l DFI   (LT8)   (VIN=8)
                               86,87 CADILLAC "C" CAR


  DATA STREAM A23
                   4.1l DFI   (LT8)   (VIN=8)
                              86,87 CADILLAC  "E" AND "K" CAR


  DATA STREAM A24
         2.0l TBI  (LL8) (VIN = 1)   87' J,L - CAR
         2.0l TBI  (LL8) (VIN = 1)   88' L - CAR  LAST 6 VIN DIGITS < 500000


  DATA STREAM A25
            2.8L PFI   (LB6)   (VIN=W)   87 "A" CARS

            2.8L PFI   (LB6)   (VIN=W)   87 "J" CARS

            2.8L PFI   (LB6)   (VIN=W)   LB6-88A "L" CARS
              (ASSEMBLY PLANTS E/Y, VIN SERIAL <500001)


  DATA STREAM A26
                 2.0L PFI-TURBO (LT3)   (VIN=M)   87, 88, 89, 90


  DATA STREAM A27
                 2.0L TBI   (LT2)   (VIN=K)   87
                 2.5L TBI   (LR8)   (VIN=R)   87, 88, 89
                 2.5L TBI   (L68)   (VIN=U)   87, 88


  DATA STREAM A28
            5.0L PFI   (LB9)   (VIN=F)   86, 87, 88
            5.7L MFI   (L98)   (VIN=8)   85, 86, 87, 88


  DATA STREAM A29
             2.8L PFI   (L44)   (VIN=9)   85, 86, 87, 88


  DATA STREAM A30
             4.3L TBI   (LB4)   (VIN=Z)   86, 87 CARS


  DATA STREAM A31
            1.6L CLCC  (L17)   (VIN=C)   81, 82, 83, 84, 85, 86, 87


  DATA STREAM A32
            2.5L PFI   (LN8)   (VIN=E)   87   S/T TRUCKS


  DATA STREAM A33
            4.3L TBI   (LB4)   (VIN=Z)   86,87,88 TRUCKS
            5.0L TBI   (L03)   (VIN=H)   87,88    TRUCKS
            5.7L TBI   (L05)   (VIN=K)   87,88    TRUCKS
            4.3L TBI   (LB4)   (VIN=Z)   91       TRUCKS



  DATA STREAM A34
            2.5L TBI   (LN8)   (VIN=E) 88,89
            2.5L TBI   (LN8)   (VIN=E) 87 S/T TRUCKS


  DATA STREAM A35
            2.8L TBI   (LL2)   (VIN=R)   86,87 TRUCKS


  DATA STREAM A36
         2.0l TBI  (LL8) (VIN = 1)   88' J - CAR
         2.0l TBI  (LL8) (VIN = 1)   88' L - CAR  LAST 6 VIN DIGITS > 500000
         2.0l TBI  (LL8) (VIN = 1)   89' J,L - CAR


  DATA STREAM A37
            2.0L TBI   (LT2)   (VIN=K)   88


  DATA STREAM A38
            2.8L PFI MAF(LB6)  (VIN=W)   88  "A" CARS CALIFORNIA EMISSIONS
            2.8L PFI MAF(LB6)  (VIN=W)   87  "A" CARS CALIFORNIA EMISSIONS
            2.8L PFI MAF(LB6)  (VIN=W)   87  "J" CARS CALIFORNIA EMISSIONS
            2.8L PFI MAF(LB6)  (VIN=W)   87  "L" CARS CALIFORNIA EMISSIONS
            2.8L PFI MAF(LB6)  (VIN=W)   88-LB6B "L" CARS CALIFORNIA EMISSIONS
              (ASSEMBLY PLANTS E/Y, VIN SERIAL >500000)  88 "L"


  DATA STREAM A39
                 2.8L PFI SD(LB6)   (VIN=W)   88  "J" CARS


  DATA STREAM A40
             2.8L TBI   (LL2)   (VIN=R) 88,89,90,91 TRUCK
             3.1L TBI   (LG6)   (VIN=D) 89 TRUCKS
             2.8L TBI   (LL2)   (VIN=R) 92 S TRUCK
             2.8L TBI   (LL2)   (VIN=R) 93 S TRUCK


  DATA STREAM A41
            5.0L TBI   (L03)   (VIN=H)   88 CAR


  DATA STREAM A42
             3800 SFI   (LN3)   (VIN=C)   88 (EXCEPT TORONADO)


  DATA STREAM A43
             5.0l CLCC  (LV2)   (VIN=Y)   88, 89, 90
             5.0l CLCC  (LG8)   (VIN=9)   88, 89, 90


  DATA STREAM A44
            2.3l MFI   (LD2)   (VIN=D)   88   (N CARS)


  DATA STREAM A45
            4.1 DFI    (LT8)   (VIN=8)   83,84,85


  DATA STREAM A46
            6.0 DFI    (L62)   (VIN=9)   81,82,83,84


  DATA STREAM A47
            4.1 DFI    (LT8)   (VIN=8)   82


  DATA STREAM A48
            2.0 TBI    (LQ5)   (VIN=6)   82
            2.0 TBI    (LR9)   (VIN=B)   82


  DATA STREAM A49
            4.3L CLCC  (LV8)   (VIN=F)   82
            5.0L CLCC  (LG4)   (VIN=H)   82


  DATA STREAM A50            NOT USED

      DATA STREAM A51
            4.1 DFI    (LC7)   (VIN=7)   87,88 'V' CAR ONLY -


  DATA STREAM A52
            4.5 DFI    (LR6)   (VIN=5)   88,89 'C'
                                         CADILLAC CAR ONLY!


  DATA STREAM A53
            2.6L TBI   (L73)   (VIN=6)   87,88,89


  DATA STREAM A54
             4.5L DFI  (LR6)   (VIN=5)   88,89 CADILLAC 'E/K' CAR ONLY


  DATA STREAM A55
            2.0L TBI   (LT2)   (VIN=K)   89
            2.5L TBI   (L68)   (VIN=U)   89


  DATA STREAM A57
                 3.1L PFI SD(LH0)   (VIN=T)   88 1/2 AWD "A" CAR ONLY
                 3.1L PFI SD(LH0)   (VIN=T)   89
                 2.8L PFI SD(LB6)   (VIN=W)   89
                 3.1L PFI SD(LH0)   (VIN=T)   90   1W ONLY
                   (ASSEMBLY PLANT 9, VIN SERIAL < 114345)
                   (ASSEMBLY PLANT 1, VIN SERIAL < 109836)
                 2.8l PFI SD(LB6)   (VIN=W)   88 "J" CARS
                 2.8l PFI SD(LB6)   (VIN=W)   87/88 "A" CARS
                 2.8l PFI SD(LB6)   (VIN=W)   87 "J" CARS
                 2.8l PFI SD(LB6)   (VIN=W)   87/88 "L" CARS
                 2.8l PFI SD(LB6)   (VIN=W)   88 "W" CARS


  DATA STREAM A58
                 4.3L TBI   (LB4)   (VIN=Z)   89  TRUCKS
                 4.3L TBI   (LB4)   (VIN=Z)   90 91 S/T TRUCKS w/autoc TRANS
                 4.3L TBI   (LB4)   (VIN=Z)   90 C/K/G/M/L/R/V TRUCKS
                 4.3L TBI   (LU2)   (VIN=B)       90 TRUCKS
                 5.0L TBI   (L03)   (VIN=H)   89, 90 TRUCKS
                 5.7L TBI   (L05)   (VIN=K)   89     TRUCKS
                 5.7L TBI   (L05)   (VIN=K)       90 TRUCKS LIGHT DUTY EMISSION
                 6.0L TBI   (LS0)   (VIN=P)   89     TRUCKS
                 7.4L TBI   (L19)   (VIN=N)   89     TRUCKS
                 7.4L TBI   (L19)   (VIN=N)       90 TRUCKS LIGHT DUTY EMISSION


  DATA STREAM A59
            5.0l PFI   (LB9)   (VIN=F)   89
            5.7l PFI   (L98)   (VIN=8)   89


  DATA STREAM A60
             5.0  CLC   (LV2)   (VIN=Y)   83


 DATA STREAM A61
            5.0  CLC   (LV2)   (VIN=Y)   82


  DATA STREAM A62
                    5.0  TBI   (LU5)   (VIN=7)   82
                    5.7  MFI   (L83)   (VIN=8)   82


  DATA STREAM A63
                    4.3  TBI   (LB4)   (VIN=Z)   85
                    5.0  CFI   (LB9)   (VIN=5)   85
                    5.7  CFI   (L83)   (VIN=8)   83, 84, 85


  DATA STREAM A64
                    1.8  CLC   (L46)   (VIN=G)   82
                    2.0  CLC   (LR9)   (VIN=B)   82,83,84
                    2.5  CLC   (LQ8)   (VIN=F)   82,83,85,86
                    2.5  CLC   (LW9)   (VIN=5)   82,83
                    2.8  CLC   (LC1)   (VIN=1)   82,83
                    2.8  CLC   (LE2)   (VIN=X)   81,82,83
                    2.8  CLC   (LH7)   (VIN=Z)   82,83
                    2.8  CLC   (LL1)   (VIN=L)   83
                    2.8  CLC   (LR2)   (VIN=B)   82,83
                    3.0  CLC   (LK9)   (VIN=E)   82,83
                    3.8  CLC   (LC3)   (VIN=9)   82,83
                    3.8  CLCT  (LC8)   (VIN=3)   82,83
                    3.8  CLC   (LD5)   (VIN=A)   82,83
                    4.1  CLC   (LC4)   (VIN=4)   82,83
                    4.4  CLC   (L39)   (VIN=J)   82
                    5.0  CLC   (LG8)   (VIN=9)   83
                    5.0  CLC   (LG4)   (VIN=H)   83
                    5.0  CLC   (LF3)   (VIN=H)   83,84
                    5.7  CLC   (LM1)   (VIN=L)   82,83
                    5.7  CLC   (LS9)   (VIN=L)   83,84
                    6.0  CLC   (L61)   (VIN=6)   81,82,83


  DATA STREAM A65
             USAGE:
            2.5 CLC    (LW9)   (VIN=5)   81
            2.8 CLC    (LH7)   (VIN=Z)   81
            3.8 CLC    (LC3)   (VIN=K)   81
            3.8  CLCT  (LC8)   (VIN=3)   81
            3.8 CLC    (LD5)   (VIN=A)   81
            4.1 CLC    (LC4)   (VIN=4)   81
            4.3 CLC    (LS5)   (VIN=S)   81
            4.3 CLC    (LV8)   (VIN=F)   81
            4.4 CLC    (L39)   (VIN=J)   81
            4.9 CLCT   (LU8)   (VIN=T)   81
            4.9 CLC    (33333333333333   81
            5.0 CLC    (LG4)   (VIN=H)   81
            5.0 CLC    (LV2)   (VIN=Y)   81
            5.7 CLC    (LM1)   (VIN=L)   81
            5.7 CLC    (L77)   (VIN=B)   81
            5.7 CLC    (L82)   (VIN=6)   81


  DATA STREAM A66
            5.0L CLCC  (LG4)   (VIN=H)   88
            5.0L CLCC  (L69)   (VIN=G)   86,87,88


  DATA STREAM A68
               USAGE:
             4.3L TBI   (LB4)   (VIN=Z)   88 CARS


  DATA STREAM A69
              USAGE:
            2.3l MFI   (LD2)   (VIN=D)   89
            2.3l MFI   (LD2)   (VIN=D)   88


  DATA STREAM A71
            3800 SFI   (LN3)   (VIN=C)   88 TORONADO


  DATA STREAM A72
                 3800 SFI   (LN3)   (VIN=C)    89  (EXCEPT TORONADO)



  DATA STREAM A73
                 3300 MFI   (LG7)   (VIN=N)   89   'N' CARS
                 3300 MFI   (LG7)   (VIN=N)   89   'A' CARS



  DATA STREAM A74
                 3.8L SFI   (LG3)   (VIN=3)   87 TORONADO


  DATA STREAM A75
            3.8L SFI   (LG3)   (VIN=3)   86 TORONADO


  DATA STREAM A76
            2.8L CLCC  (LR2)   (VIN=B)   83 CHEVY TRUCK



  DATA STREAM A77
            1.9L ISUZU (LR1)   (VIN=A)   83



  DATA STREAM A78
            6.2L DSL   (LL4)   (VIN=J)   84
            6.2L DSL   (LH6)   (VIN=C)   84


  DATA STREAM A79
            1.9L ISUZU (LR1)   (VIN=A)   84


  DATA STREAM A80
            1.9L ISUZU (LR1)   (VIN=A)   84.5


  DATA STREAM A81
            6.2L DSL   (LL4)   (VIN=J)   88
            6.2L DSL   (LH6)   (VIN=C)   88


  DATA STREAM A82
            5.7L SFI   (LT5)   (VIN=J)   89


  DATA STREAM A83
            5.0L TBI   (L03)  (VIN=E) 89, 90, 91, 92 'F'CARS


  DATA STREAM A84
            4.3L TBI   (LB4)   (VIN=Z)   89, 90 CARS


  DATA STREAM A85
            3800 SFI   (LN3)   (VIN=C)   89 TORONADO


  DATA STREAM A86
            4.5 SFI    (LQ6)   (VIN=8)   89 'V' CAR ONLY     -1G6VR3185KU100501

      DATA PIN:        L/M
      BAUD RATE :      8192

  DATA STREAM A88
            2.8L PFI MAF(LB6)  (VIN=W)   88  "W"
            2.8L PFI MAF(LB6)  (VIN=W)   88  "A" CARS FEDERAL EMISSIONS
            2.8L PFI MAF(LB6)  (VIN=W)   LB6-88B "L" CARS FEDERAL EMISSIONS
              (ASSEMBLY PLANTS E/Y, VIN SERIAL >500000)  88 "L"
            2.8L PFI MAF(LB6)  (VIN=W)   87 "A" CARS FEDERAL EMISSIONS
            2.8L PFI MAF(LB6)  (VIN=W)   87 "J" CARS FEDERAL EMISSIONS
            2.8L PFI MAF(LB6)  (VIN=W)   87 "L" CARS FEDERAL EMISSIONS


  DATA STREAM A89
              USAGE:
            2.3l MFI   (LG0)   (VIN=A)   89


  DATA STREAM A90
            5.0L TBI   (L03)   (VIN=E)   89, 90 'B' CARS
            5.7L TBI   (L05)   (VIN=7)   89     'B' CARS
            5.7L TBI   (L05)   (VIN=7)   90   'B/D' CARS


  DATA STREAM A91
                USAGE:
             3.1l PFI   (LG5)   (VIN=V)   89


  DATA STREAM A92
             USAGE:
           2.3l MFI   (LD2)   (VIN=D)   90   N CAR
           2.3l MFI   (LG0)   (VIN=A)   90   L/N CAR


  DATA STREAM A93
              USAGE:
            2.3l MFI   (LD2)   (VIN=D)   90  W CAR ONLY
            2.3l MFI   (LG0)   (VIN=A)   90  W CAR ONLY


  DATA STREAM A94
              USAGE:
            3800 SFI   (LN3)   (VIN=C)   90 91


  DATA STREAM A95
               USAGE:
             4.5L SFI   (LQ6)   (VIN=8)   90
             4.5L SFI   (LW2)   (VIN=3)   90
             4.5L SFI   (LQ6)   (VIN=8)   91  6V-CAR
             4.9L SFI   (L26)   (VIN=B)   91  6C,E,K-CAR
             4.5L SFI   (LQ6)   (VIN=8)   92  6V-CAR
             4.9L SFI   (L26)   (VIN=B)   92  6C,E,K-CAR
             4.9L SFI   (L26)   (VIN=B)   93  6C,E,K-CAR


  DATA STREAM A96
              USAGE:
            2.5  TBI   (LR8)   (VIN=R)   90 'W' CAR ONLY
            2.5  TBI   (LR8)   (VIN=R)   91 'W' CAR ONLY
            2.5  TBI   (LR8)   (VIN=R)   92 '1W' CAR ONLY


  DATA STREAM A97
              USAGE:
            2.5  TBI   (L68)   (VIN=U)   91 'N' CARS
            2.5  TBI   (L68)   (VIN=U)   90 'N' CARS
            2.5  TBI   (LR8)   (VIN=R)   90 'A' CARS
            2.5  TBI   (LR8)   (VIN=R)   91 'A' CARS
            2.5  TBI   (LR8)   (VIN=R)   92 '3,4A' CARS


  DATA STREAM A98
              USAGE:
            2.2  TBI   (LM3)   (VIN=G)   90
            2.2  TBI   (LM3)   (VIN=G)   91


  DATA STREAM A99
              USAGE:
            2.5  TBI   (LN8)   (VIN=E)   90
            2.5L TBI   (LN8)   (VIN=E)   91  S,T    TRUCKS


  DATA STREAM A100
              USAGE:
            5.0  PFI   (LB9)   (VIN=F)   90, 91,92
            5.7  PFI   (L98)   (VIN=8)   90, 91,92


  DATA STREAM A101  *********DELETED **************

  DATA STREAM A102  ***********DELETED ************

  DATA STREAM A103
              USAGE:
            3.1L TBI   (LG6)   (VIN=D)   90
            3.1L TBI   (LG6)   (VIN=D)   91
            3.1L TBI   (LG6)   (VIN=D)   92
            3.1L TBI   (LG6)   (VIN=D)   93


  DATA STREAM A104
              USAGE:
          4.3L TBI   (LB4)   (VIN=Z)   90 C/K  TRUCK   23 word data list
          4.3L TBI   (LB4)   (VIN=Z)   91 S/T  TRUCK W/MANUAL TRANSMISSION
          4.3L TBI   (LB4)   (VIN=Z)   91 C,K,G,M,L  TRUCK W/MANUAL TRANSMISSION
          4.3L TBI   (LB4)   (VIN=Z)   90 M/L/G
          4.3L TBI   (LB4)   (VIN=Z)   90 S/T  TRUCK W/MANUAL TRANSMISSION
          4.3L TBI   (LB4)   (VIN=Z)   92 C,K,S,T,M,L,G TRUCK
          4.3L TBI   (LB4)   (VIN=Z)   93 C,K TRUCK


  DATA STREAM A105  *******DELETED ************

  DATA STREAM A106
              USAGE:
            5.7L TBI   (L05)   (VIN=K)   90 HEAVY DUTY EMISSIONS
            7.4L TBI   (L19)   (VIN=N)   90 HEAVY DUTY EMISSIONS
            5.7L TBI   (L05)   (VIN=K)   91 HEAVY DUTY EMISSIONS
            7.4L TBI   (L19)   (VIN=N)   91 HEAVY DUTY EMISSIONS
            5.7L TBI   (L05)   (VIN=K)   92 HEAVY DUTY EMISSIONS
            7.4L TBI   (L19)   (VIN=N)   92 HEAVY DUTY EMISSIONS
            7.4L TBI   (L19)   (VIN=N)   93 C,K HEAVY DUTY EMISSIONS


  DATA STREAM A107
              USAGE:
            4.3L TBI   (LB4)   (VIN=Z)   90 (MD-DUTY) P TRUCK
            6.0L TBI   (LS0)   (VIN=P)   89, 90 (MD-DUTY)
            7.0L TBI   (LR0)   (VIN=M)   90 (MD-DUTY)
            4.3L TBI   (LB4)   (VIN=Z)   91 (MD-DUTY) C,K,P TRUCK
            4.3L TBI   (LB4)   (VIN=Z)   92 P TRUCK
            4.3L TBI   (LB4)   (VIN=Z)   93 (MD-DUTY) P TRUCK
            4.3L TBI   (LB4)   (VIN=Z)   94 (MD-DUTY ONLY) P TRUCK
*             4.3L TBI   (LB4)   (VIN=Z)   95 (MD-DUTY ONLY) P TRUCK



  DATA STREAM A109
              USAGE:
            3.1L PFI SD(LH0)   (VIN=T)   90   1W ONLY
              (ASSEMBLY PLANT 9, VIN SERIAL > 114344)
              (ASSEMBLY PLANT 1, VIN SERIAL > 109835)
            3.1  PFI SD(LH0)   (VIN=T)  90  1A,1J,1L,2A,2L,2W,3A,3W,4W
            3.1L PFI   (LH0)   (VIN=T)  91  4W (4 door) (vin serial < 800,000)


  DATA STREAM A110
              USAGE:
            3.1  PFI TURBO  (LG5)   (VIN=V)   90


  DATA STREAM A111 PN 93328       ASSEMBLY # 93327
              USAGE:
            Central Computer Module     90  'Y' Cars  (CCM)
            Central Computer Module     91  'Y' Cars  (CCM)


  DATA STREAM A112
              USAGE:
            3.8L MFI  (L27)   (VIN=L)   90   W car
            3.8L MFI  (L27)   (VIN=L)   91   W car
            3.8L MFI  (L27)   (VIN=L)   92   W car


  DATA STREAM A113 PN 93393       ASSEMBLY #  93392
              USAGE:
           3300 MFI   (LG7)   (VIN=N)    90    ECM
           3300 MFI   (LG7)   (VIN=N)    89    'A' CARS


  DATA STREAM A114
              USAGE:
           5.7 SFI    (LT5)   (VIN=J)   90


  DATA STREAM A115
              USAGE:
           5.7 SFI    (L98)   (VIN=8)   90  'Y' Car only
           5.7 SFI    (L98)   (VIN=8)   91  'Y' Car only


  DATA STREAM A116
              USAGE:
           1.6 TBI    (L73)   (VIN=6)   90
           1.6 TBI    (L73)   (VIN=6)   91
           1.6 TBI    (L73)   (VIN=6)   92
           1.6 TBI    (L73)   (VIN=6)   93
           1.6 TBI    (L73)   (VIN=6)   94


  DATA STREAM A117
              USAGE:
           2.0 TBI    (LT2)   (VIN=k)   89  'T' Car Only
           2.0 TBI    (LT2)   (VIN=k)   90  'T' Car Only
           2.0 TBI    (LT2)   (VIN=k)   91  'T' Car Only


  DATA STREAM A118
              USAGE:
           Body Computer Module  (bcm)  90 'Cadillac E/K' Only


  DATA STREAM A119
              USAGE:
           Body Computer Module  (bcm)  90 'Buick E' Only


  DATA STREAM A120
              USAGE:
           Body Computer Module  (bcm)  90  'Oldsmobile E' Only


  DATA STREAM A121
              USAGE:
           Body Computer Module  (bcm)  90  'Cadillac V' Only


  DATA STREAM A122
              USAGE:
           Body Computer Module  (bcm)  90  'Cadillac C' Only


  DATA STREAM A123
              USAGE:
            3.8l  SFI  (LG3)    (VIN=3)  87 'Buick E' Only


  DATA STREAM A124  *******DELETED ************



  DATA STREAM A125
              USAGE:
            Supplemental Inflatable Restraint (SIR)
              1990 Cadillac C/E/K/V
              1990 Chevrolet M/R/F
              1991 Chevrolet F
              1991 Chevrolet B
              1990-1991 Pontiac F
              1990 Oldmobile E
              1990 Buick E
              1991 Buick C
              1992 Buick H
              1992 2,3H, 1,3,4B, 3,4,6C, 3,4,6E, 1,2F, 6K, 1L, 1M, 1R, 6V, 1Y
              1993 1,3,4B 6C 6K 1L 3,4C 3,4,6E 3,4H 1Y 6V 1M 1R 3,4A


  DATA STREAM A126
              USAGE:
            1.6L MFI  (LW0)   (VIN=5)   90
            1.6L MFI  (L01)   (VIN=6)   90
            1.6L MFI  (LW0)   (VIN=5)   91
            1.6L MFI  (L01)   (VIN=6)   91
            1.6L MFI  (L01)   (VIN=6)   92


  DATA STREAM A127
              USAGE:
            7.4L TBI  (L19)   (VIN=N)   87, 88 TRUCKS

  DATA STREAM A128          not used



  DATA STREAM A129
              USAGE:
            5.0L        L03     (VIN=E)   91 B,gm300, D
            5.7L        L05     (VIN=7)   91 B,gm300, D
            5.7L        L05     (VIN=7)   92 B,gm300, D
            4.3L        LB4     (VIN=Z)   92 1B
            5.0L        L03     (VIN=E)   92 1,3,4B 1,6D
            5.7L        L05     (VIN=7)   93 1B,3B,4B
            5.0L        L03     (VIN=E)   93 1B,F 2F 3B
            4.3L        LB4     (VIN=Z)   93 1B


  DATA STREAM A130
              USAGE:
              3.8L TPI  (L27)   (VIN=L)   91  C  CAR ONLY
              3.8L TPI  (L27)   (VIN=L)   92  H  CAR ONLY
              3.8L TPI  (L27)   (VIN=L)   92  C  CAR ONLY


  DATA STREAM A131
        ENGINE OIL LIFE MONITOR (EOLM) USAGE:
                                               91 C-CAR
                                               92 H-CAR
                                               92 C-CAR
                                               93 4C,H 3,4B-CARS


  DATA STREAM A132
        REMOTE ACCESSORY CONTROL MODULE (RAC) USAGE:
                                               91 C-CAR
                                               92 H-CAR
                                               92 C-CAR
                                               93 3,4C 2,3,4H-CAR



  DATA STREAM A133
        4WAL
        CAR LINE:
                 90,91,92  M,L & S,T(4 DOOR)
                 93        L 3T



  DATA STREAM A134
       BOSCH ABS
       CAR LINE:
           1990 Y, B, D, E, & K Cars
           1991 Y,B & E Cars
           1992 B car
           1992 3,4E, 6E,K
           1993 B, 3,4E, 6E CARS


  DATA STREAM A135
       ENGINE USAGE:
              2.0L OHC TBI   LT2 (VIN=K)      1990  J CAR
              2.0L OHC TBI   LT2 (VIN=K)      1991  J CAR


  DATA STREAM A136
       ENGINE USAGE:
              3.1L TBI   (LG6)   (VIN=D)   91 U VAN
              3.1L TBI   (LG6)   (VIN=D)   92 U VAN
              3.1L TBI   (LG6)   (VIN=D)   93 U VAN
              3.1L TBI   (LG6)   (VIN=D)   94 U VAN
              3.1L TBI   (LG6)   (VIN=D)   95 U VAN


  DATA STREAM A137
       ENGINE USAGE:
              6.0L TBI   (LS0)   (VIN=P) 91
              7.0L TBI   (LR0)   (VIN=M) 91
              6.0L TBI   (LS0)   (VIN=P) 92 GMT530 TRUCK
              7.0L TBI   (LR0)   (VIN=M) 92 GMT530 TRUCK
              6.0L TBI   (LS0)   (VIN=P) 93 GMT530 TRUCK
              7.0L TBI   (LR0)   (VIN=M) 93 GMT530 TRUCK
              6.0L TBI   (LS0)   (VIN=P) 94 GMT530 TRUCK
              7.0L TBI   (LR0)   (VIN=M) 94 GMT530 TRUCK
*           6.0L TBI   (LS0)   (VIN=P) 95 GMT530 TRUCK
*           7.0L TBI   (LR0)   (VIN=M) 95 GMT530 TRUCK


  DATA STREAM A138
       ENGINE USAGE:                PCM6 4L80E
              4.3L TBI    LB4   (VIN=Z)   91,92,93
              5.7L TBI    L05   (VIN=K)   91,92,93
              7.4L TBI    L19   (VIN=N)   91,92,93


  DATA STREAM A139
       ENGINE USAGE:
              2.5L  TBI L38  (VIN=A)   1991  S-TRUCKS
              2.5L  TBI L38  (VIN=A)   1992  S-TRUCKS
              2.5L  TBI L38  (VIN=A)   1993  S-TRUCKS


  DATA STREAM A140
       ENGINE USAGE:
            3.1L PFI   (LH0)   (VIN=T)   91   W,A,J,L - CAR
            3.1L PFI   (LH0)   (VIN=T)   91   4W (4 door) (vin serial > 799,999)
            3.1L PFI   (LH0)   (VIN=T)   92    1,2,3,4W, 1,2J, 1,7L - cars
            3.1L PFI   (LH0)   (VIN=T)   93    1J,L,2J,1,2,3W cars
            3.1L PFI   (LH0)   (VIN=T)   94    1,2J


  DATA STREAM A141
       ENGINE USAGE:
              3.4L PFI   (LQ1)   (VIN=X)   91           W-CAR


  DATA STREAM A142
       ENGINE USAGE:
              5.7 SFI - LT5 (VIN=J)  1991


  DATA STREAM A143
       ENGINE USAGE:
              3300 MFI   (LG7)   (VIN=N)    91    A,N-CAR
              3300 MFI   (LG7)   (VIN=N)    92    3,4A 2,3,4N CARS
              3300 MFI   (LG7)   (VIN=N)    93    3,4A 2,3,4N CARS


  DATA STREAM A144
       ENGINE USAGE:
              2.3l MFI   (LD2)   (VIN=D)   91   N CAR
              2.3l MFI   (LG0)   (VIN=A)   91   L/N CAR


  DATA STREAM A145
       ENGINE USAGE:
              2.3l MFI   (LD2)   (VIN=D)   91   W CAR


  DATA STREAM A146
       BCM USAGE:
       CAR LINE:
           1991 GM30/33 (RIVIERA/REATTA)    (VIN=E)


  DATA STREAM A147
       BCM USAGE:
       CAR LINE:
           1991     TORONADO AND TORONADO TROFEO  (BODY VIN=E)


  DATA STREAM A148
       ENGINE USAGE:  DIGITAL EGR
              3.1  PFI   (LH0)   (VIN=T)  90  1F, 2F
              3.1 PFI    (LH0)   (VIN=T)  91  1F, 2F
              3.1 PFI    (LH0)   (VIN=T)  92  1F, 2F

  DATA STREAM A149     not used


  DATA STREAM A150
       TCM USAGE: THE R2 TRANSMISSION CAN BE USED WITH THE FOLLOWING ENGINES
              4.3L TBI    LB4   (VIN=Z)   91
              5.7L TBI    L05   (VIN=K)   91
              7.4L TBI    L19   (VIN=N)   91

  DATA STREAM A151
       BCM USAGE :
       CAR LINE  :
           1991 GM35 (ALLANTE)     VIN = V
           1992 GM35 (ALLANTE)     VIN = V


  DATA STREAM A152
       BCM USAGE :
       CAR LINE  :
           1991 GM30 (ELDORADO/SEVILLE) (VIN=E/K)


  DATA STREAM A153
       BCM USAGE :
       CAR LINE  :
              1991 DEVILLE/FLEETWOOD (VIN=C)
              1992 DEVILLE/FLEETWOOD (VIN=C)
              1993 DEVILLE/FLEETWOOD (VIN=C)


  DATA STREAM A154
       ENGINE   USAGE:
              3.8L TPI  (L27)   (VIN=L)   91  E  CAR ONLY
              3.8L TPI  (L27)   (VIN=L)   92  E  (Riviera, Toronado & Trofeo)
              3.8L TPI  (L27)   (VIN=L)   93  E  (Riviera, Toronado & Trofeo)


  DATA STREAM A155
       TEVES ABS/ASR USAGE:
       CAR LINE  :
              1991      Buick C-car
              1991      3C,6C-car
              1992      H-cars
              1992      3,4C,6C-cars
              1993      H, 3,4C, 6C CARS



  DATA STREAM A156
       DELCO 6 ABS
       USAGE:  1991 N CAR
               1992 2J, 1L, 2,3,4N cars


  DATA STREAM A157
       DIC USAGE :  1991 OLDSMOBILE C-CAR
                    1992 OLDSMOBILE H-CAR
                    1992 OLDSMOBILE C-CAR
                    1993 OLDSMOBILE H-CAR
                    1993 OLDSMOBILE C-CAR



  DATA STREAM A158   not used


  DATA STREAM A159
       TCM USAGE: THE R2 TRANSMISSION WITH STAND ALONE TCM  91'
                  L57  6.5L       VIN = Y      1993  C,K,G,P


  DATA STREAM A160
   ENGINE USAGE:
              4.3L TURBO (LB4)    (VIN=Z) 91.5   SYCLONE TRUCK


  DATA STREAM A161
   ENGINE USAGE:
              1.9L MFI   (LL0)   (VIN=7)   91
              1.9L TBI   (LK0)   (VIN=9)   91


  DATA STREAM A162
   ENGINE USAGE:
              3.1L PFI   (LH0)    (VIN=T) 91   1W-CAR   (VFV)


  DATA STREAM A163
   ENGINE USAGE:
       3.8L  SUPER CHARGED L67 (VIN=1)    1992 PONTIAC H-CAR
       3.8L  SUPER CHARGED L67 (VIN=1)    1992 3,4C - CAR
       3.8L                L27 (VIN=L)    1992 1,2,3U - van
       3.8L  SUPER CHARGED L67 (VIN=1)    1993 PONTIAC H-CAR
       3.8L  SUPER CHARGED L67 (VIN=1)    1993 3,4C - CAR


  DATA STREAM A164
       HVAC USAGE:
           1992 Buick H-car (2,3,4H)
           1992 3,4C-car
           1993 3,4C 2,3,4H -car


  DATA STREAM A165
       DRIVER/PASSENGER DERM (SIR)
       USAGE:  1992 H CAR
               1993 6E 6K 6D 2,3F 2H

  DATA STREAM A166      not used


  DATA STREAM A167
   ENGINE USAGE:
       2.2L  MFI LN2    (VIN=4)           1992 1J,L
       2.2L  MFI LN2    (VIN=4)           1993 1J,L,W,3A,4A


  DATA STREAM A168
   ENGINE USAGE:
       2.0L  MFI LE4    (VIN=H)           1992 2J, 7T
       2.0L  MFI LE4    (VIN=H)           1993 2J
       2.0L  MFI LE4    (VIN=H)           1994 2J


  DATA STREAM A169
   ENGINE USAGE:
       2.3L  MFI DOHC       LD2    (VIN=D)           1992 2,3N
       2.3L  MFI OHC        L40    (VIN=3)           1992 2,3,4N
       2.3L  MFI DOHC H.O.  LG0    (VIN=A)           1992 2,3N, 1,7L


  DATA STREAM A170
   ENGINE USAGE:
       2.3L  MFI DOHC       LD2    (VIN=D)           1992 2,3W


  DATA STREAM A171
   ENGINE USAGE:
       5.7L  SFI OHC        LT5    (VIN=J)           1992 1Y


  DATA STREAM A172
   ENGINE USAGE:
       5.7L  MFI H.O.       LT1    (VIN=P)           1992 1Y
       5.7L  MFI H.O.       LT1    (VIN=P)           1993 1Y 1,2F


  DATA STREAM A173
   USAGE:
       Central Computer Module     92  'Y' Cars  (CCM)
                                   93  'Y' Cars  (CCM)


   DATA STREAM A174
        DELCO 6 ABS
        USAGE:
                1992 1,2,3U van 1,2,3,4W car


  DATA STREAM A175
       BOSCH ABS/ASR
       CAR LINE:
                 1992 Y CAR
                 1993 Y CAR
                 1994 Y CAR


  DATA STREAM A176
       ENGINE   USAGE:
              3.8L TPI  (L27)   (VIN=L)   92  E  (Reatta only)


  DATA STREAM A177
       TCM USAGE: THE R2 TRANSMISSION CAN BE USED WITH THE FOLLOWING ENGINES
              4.3L TBI    LB4   (VIN=Z)   92,93
              5.7L TBI    L05   (VIN=K)   92,93
              7.4L TBI    L19   (VIN=N)   92,93


  DATA STREAM A178
       ENGINE   USAGE:
              4.3L CPI  (L35)   (VIN=W)   92  M,L,S,T TRUCK
              4.3L CPI  (L35)   (VIN=W)   94  M,L,S,T TRUCK


  DATA STREAM A179
       ENGINE   USAGE:
                 5.0L TBI   (L03)   (VIN=H)   92  C,K,G TRUCKS
                 5.7L TBI   (L05)   (VIN=K)   92  C,K,G,R,V TRUCKS
                   5.0L TBI   (L03)   (VIN=H)   93 C,K        TRUCKS
                   5.7L TBI   (L05)   (VIN=K)   93 C,K,P      TRUCKS
                   5.0L TBI   (L03)   (VIN=H)   94 C,K        TRUCKS
                   5.7L TBI   (L05)   (VIN=K)   94 C,K,P      TRUCKS
*                  5.0L TBI   (L03)   (VIN=H)   95 C,K        TRUCKS
*                  5.7L TBI   (L05)   (VIN=K)   95 C,K,P      TRUCKS


  DATA STREAM A180
       BCM USAGE:
       CAR LINE:
           1992 GM30/33 (RIVIERA/REATTA)    (VIN=E)
           1993 GM30/33 (RIVIERA/REATTA)    (VIN=E)


  DATA STREAM A181
       BCM USAGE:
       CAR LINE:
              1992     TORONADO AND TORONADO TROFEO  (BODY VIN=E)
              1993     TORONADO AND TORONADO TROFEO  (BODY VIN=E)



  DATA STREAM A182
       BCM USAGE:
       CAR LINE:
   NOTE: DELETED 92 USAGE SEE DATA STREAM A153
              1992 DEVILLE/FLEETWOOD (VIN=C)


  DATA STREAM A183
       IPC USAGE:
       CAR LINE:
              1992 ELDORADO/SEVILLE  (VIN=E/K)


  DATA STREAM A184
   ENGINE USAGE:
       1.8L  PFI            LV6    (VIN=8)           1992 1,7R
       1.8L  PFI            LV6    (VIN=8)           1993 1,7R


  DATA STREAM A185   not used


  DATA STREAM A186
   ENGINE USAGE:
              3.4L PFI   (LQ1)   (VIN=X)   92           W-CAR
              3.4L PFI   (LQ1)   (VIN=X)   93           W-CAR
              3.1L PFI   (LH0)   (VIN=T)   93    1W,2W,3W,4W -CAR
              3.1L PFI   (LH0)   (VIN=T)   94           1W


  DATA STREAM A187
   ENGINE USAGE:
              3.1L PFI   (LH0)    (VIN=T) 92   1W-CAR   (VFV)


  DATA STREAM A188
   ENGINE USAGE:
              4.3L TBI   (LB4)    (VIN=Z) 93 VCM S,T TRUCK


  DATA STREAM A189
        4WAL
        CAR LINE:
                   92 3-SENSOR C,K, TRUCK
                   93 3-SENSOR C,K,G TRUCK
                   93 3-SENSOR S,T & M,L TRUCK AND BUS
                   94 3-SENSOR C,K,G,M,L,S,T TRUCK
                   95 3-SENSOR C,K,G,M,L,S,T TRUCK


  DATA STREAM A190
          RWAL:
              4.3L TBI   (LB4)    (VIN=Z) 93 VCM S,T TRUCK


  DATA STREAM A191
           HVAC:
              4.3L TBI   (LB4)    (VIN=Z) 93 VCM S,T TRUCK


  DATA STREAM A192
   ENGINE USAGE:
              4.3L TBI   (LB4)    (VIN=Z) 94 VCM S,T TRUCK
              4.3L TBI   (LB4)    (VIN=Z) 95 VCM S,T TRUCK


  DATA STREAM A193
          FWAL:
              4.3L TBI   (LB4)    (VIN=Z) 94 VCM S,T TRUCK
              4.3L TBI   (LB4)    (VIN=Z) 95 VCM S,T TRUCK



  DATA STREAM A194
           HVAC:
              4.3L TBI   (LB4)    (VIN=Z) 94 VCM S,T TRUCK
              4.3L TBI   (LB4)    (VIN=Z) 95 VCM S,T TRUCK


  DATA STREAM A195
          ENGINE USAGE:
              5.7L TBI   (L05)    (VIN=K) 92 VCM CNG VEHICLE


  DATA STREAM A196
       TCM USAGE:   THE R2 TRANSMISSION WITH STAND ALONE TCM  92'
*                 LL4  6.2L       VIN = J      1992  C,K
*                 L65  6.5L       VIN = F      1992  C,K
*                 LL4  6.2L       VIN = J      1993  C,K
*                 L65  6.5L       VIN = F      1993  C,K


   DATA STREAM A197
        DELCO 6 ABS
        USAGE:
                1993 1,2,3U van 1,2,3,4W car


   DATA STREAM A198
        DELCO 6 ABS
        USAGE:
                1993 1,2F CAR


   DATA STREAM A199
        DELCO 6 ABS
        USAGE:
                1993 1S CAR


  DATA STREAM A200
          ENGINE USAGE:
              1.6L PFI   (L01)    (VIN=6) 93 R CAR ONLY


  DATA STREAM A201
          ENGINE USAGE: PCM-6 4L60E
              L03    5.0L       VIN = H   93 C,K,G
              L05    5.7L       VIN = K   93 C,K,G
              L35    4.3L       VIN = W   93 S,T,M,L
              LB4    4.3L       VIN = Z   93 G,M,L,S,T,C,K


   DATA STREAM A202
        DELCO 6 ABS
        USAGE:
                1993 1,2J 1,7L 2,3,4N CARS


  DATA STREAM A203
   ENGINE USAGE:
       2.3L  PFI DOHC       LD2    (VIN=D)           1993 2,3N
       2.3L  PFI OHC        L40    (VIN=3)           1993 2,3,4N
       2.3L  PFI DOHC H.O.  LG0    (VIN=A)           1993 1L 2,3N


  DATA STREAM A204
       TCM USAGE: PCM-6 4L60E
              4.3L TBI    LB4   (VIN=Z)   93
              4.3L TBI    L35   (VIN=W)   93
              5.0L TBI    L03   (VIN=H)   93
              5.7L TBI    L05   (VIN=K)   93


  DATA STREAM A205
          ENGINE USAGE:
              3.8L SFI   (L27)    (VIN=L) 93 3,4C 2,3,4H 4W 1,2,3U


  DATA STREAM A206
       IPC USAGE:
       CAR LINE:
              1993 ELDORADO/SEVILLE  (VIN=E/K)


  DATA STREAM A207
   ENGINE USAGE:
       5.7L  SFI OHC        LT5    (VIN=J)           1993 1Y
       5.7L  SFI OHC        LT5    (VIN=J)           1994 1Y
       5.7L  SFI OHC        LT5    (VIN=J)           1995 1Y


  DATA STREAM A208
       BOSCH ABS/ASR
       CAR LINE:
                 1993 6D CAR
                 1994 6D CAR


  DATA STREAM A209
       BOSCH ABS/ASR
       CAR LINE:
                 1993 6E/K 6 K SPECIAL w/137-ID8 6V CARS



  DATA STREAM A210
       CAR LINE:
              4.6L MFI   (L37)   (VIN=9)   92.5 6V,E,K
              4.6L MFI   (LD8)   (VIN=Y)   93   6V


  DATA STREAM A211
       BCM USAGE:                        (dcm)(ccm)
       CAR LINE:
              1993    BROUGHAM  (VIN = D)
              1994    BROUGHAM  (VIN = D)
              1995    BROUGHAM  (VIN = D)


  DATA STREAM A212
       BCM USAGE:
       CAR LINE:
              1993    ALLANTE  (VIN = V)
              1994    ALLANTE  (VIN = V)


  DATA STREAM A213
       ECM USAGE:
       CAR LINE:
              1993  5.7l L05   (VIN = 7)    1993 6D - CAR


  DATA STREAM A214
       ECM USAGE:
       CAR LINE:
              3.1L SFI (LH0/GENIIS/VIN=T)   93  1W,2W,3W,4W 4T60E AND NB2 ONLY



  DATA STREAM A215
       ECM USAGE:
       CAR LINE:
              3.4L SFI (L32)  (VIN = S)  93  1,2F ALL


  DATA STREAM A216
       TCM USAGE: PCM-6 4L60E DIESEL
              6.2L        LH6   (VIN=C)   93      C,K,G


  DATA STREAM A217
            PCM-6 WITH 4L60E TRANSMISSION
       ENGINE   USAGE:
                      L03        5.0L    94  VIN = H   C,K,G
                      L05        5.7L    94  VIN = K   C,K,G
                      L35        4.3L    94  VIN = W   S,T,M,L
                      LB4        4.3L    94  VIN = Z   G,M,L,S,T,C,K
                   *  L03    TBI  5.0L   95  VIN=H   C,K,G
                   *  L05    TBI  5.7L   95  VIN=K   C,K,G
                   *  L35    CPI  4.3L   95  VIN=W   S,T,M,L
                   *  LB4    TBI  4.3L   95  VIN=Z   G,M,L,S,T,C,K


  DATA STREAM A218
            PCM-6 WITH 4L60E TRANSMISSION
         The 4L60E transmission can be used with the following engines
       TCM USAGE:
           L03    TBI  5.0L   94  VIN = H   C,K,G
           L05    TBI  5.7L   94  VIN = K   C,K,G
           L35    CPI  4.3L   94  VIN = W   S,T,M,L
           LB4    TBI  4.3L   94  VIN = Z   G,M,L,S,T,C,K
                      LN2  MFI   2.2L    94  VIN=4   S
                   *  L03  TBI   5.0L    95  VIN=H   C,K,G
                   *  L05  TBI   5.7L    95  VIN=K   C,K,G
                   *  L35  CPI   4.3L    95  VIN=W   S,T,M,L
                   *  LB4  TBI   4.3L    95  VIN=Z   G,M,L,S,T,C,K
                   *  LN2  MFI   2.2L    94  VIN=4   S


  DATA STREAM A219
            PCM-6 WITH 4L80E TRANSMISSION
       ENGINE   USAGE:
                  LB4  TBI  4.3L  94   VIN = Z   C,K,G,P
                  L05  TBI  5.7L  94   VIN = K   C,K,G,P,W-MD
                  L19  TBI  7.4L  94   VIN = N   C,K,G,P
               *  LB4  TBI  4.3L 1995  VIN = Z   C,K,G,P
               *  L05  TBI  5.7L 1995  VIN = K   C,K,G,P,W-MD
               *  L19  TBI  7.4L 1995  VIN = N   C,K,G,P
               *  LB4  TBI  4.3L 1995  VIN = Z   C,K (HD)   MANUAL TRANS.
               *  L19  TBI  7.4L 1995  VIN = N   C,K (HD)   MANUAL TRANS. pcm-6


  DATA STREAM A220
            PCM-6 WITH 4L80E TRANSMISSION
        The 4L80E transmission can be used with the following engines
       TCM USAGE:
                  LB4  TBI  4.3L  94   VIN = Z   C,K,G,P
                  L05  TBI  5.7L  94   VIN = K   C,K,G,P
                  L19  TBI  7.4L  94   VIN = N   C,K,G,P
                  L05  TBI  5.7L  94   VIN = A   MEDIUM DUTY TRUCK
               *  LB4  TBI  4.3L  95   VIN = Z   C,K,G,P
               *  L05  TBI  5.7L  95   VIN = K   C,K,G,P
               *  L05  TBI  5.7L  95   VIN = A   MEDIUM DUTY TRUCK
               *  L19  TBI  7.4L  95   VIN = N   C,K,G,P


  DATA STREAM A221
   ENGINE USAGE:
       3.8L  SFI  (L27) (VIN = L)    1994 3,4C, 2,3,4H, 4W 1,2,3U
       3.8L  SFI  (L67) (VIN = 1)    1994 3,4C, 2H
       3.8L  SFI  (L67) (VIN = 1)    1995 3G
*      3.8L  SFI  (L67) (VIN = 1)    1995 3,4C, 2H
*      3.8L  SFI  (L27) (VIN = L)    1995 3,4H 4W 1,2,3U


  DATA STREAM A222
   ENGINE USAGE:    WITH M13 (4 SPD AUTO TRANS)
         2.3L  PFI DOHC       LD2    (VIN=D)   1994 2,3N
         2.3L  PFI OHC        L40    (VIN=3)   1994 2,3,4N
*        2.3L  PFI DOHC       LD2    (VIN=D)   1995 2,3N


  DATA STREAM A223
   ENGINE USAGE:
       5.7L  MFI  (LT1) (VIN = P)    1994 1B,F,Y 2F 4B 6D - CARS
       3.4L  MFI  (L99) (VIN = T)    1994 1B - CARS
*      5.7L  SFI  (LT1) (VIN = P)    1995 1Y - CAR AUTOMATIC TRANSMISSION


  DATA STREAM A224     not used


  DATA STREAM A225
       PCME DIESEL
       PCM USAGE:
           L49    PFI  6.5L         VIN = P 1994  C,K,G   4L60E/MANUAL TRANS.
           L56    PFI  6.5L TURBO   VIN = S 1994  C,K
           L65    PFI  6.5L TURBO   VIN = F 1994  C,K,P   MANUAL TRAN.
        *   L49    PFI  6.5L         VIN = P  1995  C,K,G   4L60E/MANUAL TRANS.
        *   L56    PFI  6.5L TURBO   VIN = S  1995  C,K     4L80E
        *   L65    PFI  6.5L TURBO   VIN = F  1995  C,K,P   MANUAL TRANS.


  DATA STREAM A226
       4L80E DIESEL TRANS.
       PCME USAGE:
            L49    PFI  6.5L         VIN = P 1994  C,K,G   4L60E/MANUAL TRANS.
            L56    PFI  6.5L TURBO   VIN = S 1994  C,K
         *  L49    PFI  6.5L         VIN = P  1995  C,K,G   4L60E/MANUAL TRANS.
         *  L56    PFI  6.5L TURBO   VIN = S  1995  C,K     4L80E


  DATA STREAM A227
   ENGINE USAGE:
              3.1L SFI   (L82)   (VIN=M)   93  SFI-66U  3W


  DATA STREAM A228
   ENGINE USAGE:
              4.9L SFI   (L26)   (VIN=B)   94  6E,K,Ksp - CAR
              4.9L SFI   (L26)   (VIN=B)   95  K,Ksp - CAR



* DATA STREAM A229
   DIC USAGE:
              1995       3G - CAR


  DATA STREAM A230
       HVAC USAGE:
              1994             1,4B CAR
              1994             6D     CAR
*             1995             4B  CAR
*             1995             6D  CAR


  DATA STREAM A231
       HVAC USAGE:
              1994             3C,H CAR
              1994             4C,H CAR
              1994             2H   CAR
*             1995             3,4C 2,3,4H CAR


  DATA STREAM A232
       HVAC USAGE:
              1995             3,4G - CAR


  DATA STREAM A233
       RAC USAGE:
                 1994          2,3,4H 3,4C 3W
*                1995          3,4G
*                1995   2,3,4H 3,4C 3W


  DATA STREAM A234
       IPC USAGE:
              1994             3C,H CAR
*             1995             3C,H CAR


* DATA STREAM A235
       IPC USAGE:
              1995             3G - CAR


* DATA STREAM A236
       IPC USAGE:
              1995             4G   CAR


  DATA STREAM A237
       IPC USAGE:
              1994 CADILLAC ELDORADO/SEVILLE   (VIN = E)
              1995 CADILLAC ELDORADO/SEVILLE   (VIN = E)


  DATA STREAM A238
       RTD USAGE:
                 1994   6E,K - CAR



  DATA STREAM A239
       CCM USAGE:
                 1994 "Y" CAR WITH 5.7L (LT1) (VIN=P) AND  5.7L  (LT5) (VIN=J)



  DATA STREAM A240              TEVES ABS/ASR
       ABS/ASR USAGE:
                     1994    2,3,4H 3,4C
*                    1995    3,4G
                     1995    2,3,4H 3,4C


  DATA STREAM A241          BOSCH ABS
       CAR LINE:
                1994   1,4B 6E,K,Ksp - CARS


  DATA STREAM A242
       94' REDESIGN DERM (SIR) DRIVER OR DRIVER/PASSENGER
       USAGE:
             1993  M/L
             1994  3,4C 2,3,4H 3,4A 2,3,4N 1,2,3U 1Y 1M 1R
                   1W 1Z 1,2F 6E 6K 6V 1L G-VAN M/L TRUCK
*            1995  3,4G
*        1995  1,2F 1L 3,4A 2,3,4N 1,2,3U 1Y
               M,L,S,T,G TRUCK


  DATA STREAM A243
      ENGINE USAGE:
              3.1L PFI   (L64)    (VIN=W) 93   1W-CAR   (VFV)


  DATA STREAM A244
       BOSCH ABS/ASR
       CAR LINE:  1994   6Ksp W/L26 ENGINE


   DATA STREAM A245
        DELCO 6 ABS
        USAGE:
                1994 1S CAR
                1995 1S CAR


   DATA STREAM A246
        DELCO 6 ABS/EVO
        USAGE:
               1994 1,2J 1L 2,3,4N
    ##      1995 2,3,4N ABS AND VES CARS
            1995 1L, 4N ABS ONLY


   DATA STREAM A247
        DELCO 6 ABS
        USAGE:
                   1994 1,2,3,4W 1,2,3U 3,4A
           1995 1W ABS ONLY CARS


   DATA STREAM A248      not used


   DATA STREAM A249
        DELCO 6 ABS
        USAGE:
                   1994 1,2F


   DATA STREAM A250
        DELCO 6 ABS/ASR
        USAGE:
                   1994 1,2F
                   1995 1,2F


   DATA STREAM A251
        DELCO 6 ABS/ASR
        USAGE:
                   1994 1,2,3U
                   1995 1,2,3U


   DATA STREAM A252
        DELCO SDMA/SIR
        USAGE:
            1994        1,4B 6D 1,2W  CAR
*           1995        2,3,4H 3,4C 1,4B 6D 1W CAR


  DATA STREAM A253
       CAR LINE:
              4.6L MFI   (L37)   (VIN=9)   93  6E,K
              4.6L MFI   (LD8)   (VIN=Y)   93  6E


  DATA STREAM A254
       CAR LINE:
              4.6L MFI   (L37)   (VIN=9)   94  6E,K,Ksp
*             4.6L SFI   (L37)   (VIN=9)   95   6E,K
              4.6L MFI   (LD8)   (VIN=Y)   94  6E
*             4.6L SFI   (LD8)   (VIN=Y)   95   6E,K,Ksp


* DATA STREAM A255
       CAR LINE:
              4.0L MFI   (L47)   (VIN=c)   95  3G


  DATA STREAM A256
       ENGINE USAGE:
              3.1L SFI   (L82)   (VIN=M)   94  SFI-66U  1L


  DATA STREAM A257
          F-CAR WITH ELECTRONIC TRANSMISSION (4L60E)
       ENGINE USAGE:
              3.4L SFI   (L32)   (VIN=S)   94' SFI-66U  1,2F


  DATA STREAM A258
          F-CAR WITH MANUAL TRANSMISSION
       ENGINE USAGE:
              3.4L SFI   (L32)   (VIN=S)   94' SFI-66U  1,2F


  DATA STREAM A259
       ENGINE USAGE:
              3.1L SFI   (L82)   (VIN=M)   94  SFI-66U  2,3,4N
*             3.1L SFI   (L82)   (VIN=M)   95  SFI-66U  2,3,4N


  DATA STREAM A260
          W-CAR WITH ELECTRONIC TRANSMISSION (4T60E)
       ENGINE USAGE:
              3.1L SFI   (L82)   (VIN=M)   94  SFI-66U  1,2,3,4W
*             3.1L SFI   (L82)   (VIN=M)   95  SFI-66U  1,2,3,4W


  DATA STREAM A261
          W-CAR WITH AUTO 3 SPEED TRANSMISSION
       ENGINE USAGE:
              3.1L SFI   (L82)   (VIN=M)   94  SFI-66U  1,2,3,4W
*             3.1L SFI   (L82)   (VIN=M)   95  SFI-66U  1,2,3,4W


  DATA STREAM A262           not used


  DATA STREAM A263
       ENGINE USAGE:
              3.1L  SFI  (L82) (VIN = M)    1994   3,4A
*      3.1L  SFI  (L82) (VIN = M)    1995   3,4A


  DATA STREAM A264
       ENGINE USAGE:
              3.4L  SFI  (LQ1) (VIN = X)    1994   1,2,3W
*      3.4L  SFI  (LQ1) (VIN = X)    1995   1,2,3W


  DATA STREAM A265
       ENGINE USAGE:
              LN2  MFI   2.2L    94  VIN = 4   S/T TRUCK
              LN2  MFI   2.2L    95  VIN = 4   S/T TRUCK


  DATA STREAM A266          not used


  DATA STREAM A267
       ENGINE USAGE:
              LH6 DIESEL 6.2L   (VIN=C)   93   C,K,G


  DATA STREAM A268
       TCM USAGE:
                  L57 DIESEL 6.5L        94  VIN = Y   P,G
                * L57 DIESEL 6.5L        95  VIN = Y   P,G


  DATA STREAM A269
       ENGINE USAGE:
         2.3L  PFI OHC        L40    (VIN=3)   1994 2,3,4N
         2.3L  PFI DOHC H.O.  LG0    (VIN=A)   1994 1L 2,3N
         2.2L  PFI            LN2    (VIN=4)   1994 1J,L, 3,4A
*        2.2L  PFI            LN2    (VIN=4)   1995 1J,L,W 3,4A


  DATA STREAM A270   not assigned
  DATA STREAM A271   not assigned
  DATA STREAM A272   not assigned


  DATA STREAM A273
   ENGINE USAGE:
       5.7L  MFI  (LT1) (VIN = P)    1994 1,2F - CARS MANUAL TRANSMISSION
*      5.7L  SFI  (LT1) (VIN = P)    1995 1,2F - CARS MANUAL TRANSMISSION


  DATA STREAM A274
   ENGINE USAGE:
       5.7L  MFI  (LT1) (VIN = P)    1994 1,2F - CARS AUTOMATIC TRANSMISSION
*      5.7L  SFI  (LT1) (VIN = P)    1995 1,2F - CARS AUTOMATIC TRANSMISSION


  DATA STREAM A275
   ENGINE USAGE:
       5.7L  MFI  (LT1) (VIN = P)    1994 1Y - CAR MANUAL TRANSMISSION
*      5.7L  SFI  (LT1) (VIN = P)    1995 1Y - CAR MANUAL TRANSMISSION


  DATA STREAM A276
   ENGINE USAGE:
       5.7L  SFI  (LT1) (VIN = P)    1994 1,4B 6D - CARS
       4.3L  SFI  (L99) (VIN = T)    1994 1B - CAR
*      5.7L  SFI  (LT1) (VIN = P)    1995 1,4B 6D - CARS
*      4.3L  SFI  (L99) (VIN = W)    1995 1B - CAR


  DATA STREAM A277
   ENGINE USAGE:
              3.1L SFI   (L82)   (VIN=M)   95  SFI-66U  1L


  DATA STREAM A278
   ENGINE USAGE:
              3.4L SFI   (L32)   (VIN=S)   95' SFI-66U  1,2F


  DATA STREAM A279   not assigned


  DATA STREAM A280
   ENGINE USAGE:
       3.8L  SFI  (L36) (VIN = K)    1995 3,4C, 2,3H, 4G


  DATA STREAM A281
        BOSCH ABS 5
        USAGE:
                1995   1,4B - CARS


  DATA STREAM A282  NOT USED      (PROGRAM CANCELED)
        BOSCH ABS 5
        USAGE:
                1995   6Ksp - CARS


   DATA STREAM A283
        DELCO 6 ABS
        USAGE:
              1995 1M


   DATA STREAM A284
        DELCO 6 ABS/TCS   (VES DROPPED)
        USAGE:
            1995 1, 2J ABS CARS
            1995 2J ABS/TCS CARS ONLY


   DATA STREAM A285
        DELCO 6 ABS/TCS   (VES DROPPED)
        USAGE:
            1995 2,3,4W  ABS AND VES ONLY CARS


   DATA STREAM A286
        DELCO 6 ABS
        USAGE:
            1995 1,2F ABS


  DATA STREAM A287
       BOSCH ABS/TCS
       CAR LINE:  1995   6E/K/KSP CARS


  DATA STREAM A288
       BOSCH ABS/TCS
       CAR LINE:  1995 Y CARS


  DATA STREAM A289   not assigned


  DATA STREAM A290
       BOSCH ABS/TCS
       CAR LINE:  1995 D CARS


  DATA STREAM A291   not assigned
  DATA STREAM A292   not assigned


   DATA STREAM A293
        DELCO 6 ABS
        USAGE:
            1995 3,4A  2,3,4W  1,2,3U ABS ONLY CARS


   DATA STREAM A294

        IPC USAGE:
               1995    1,2J


   DATA STREAM A295
        DELCO SDM B/SIR
        USAGE:
             1995      2,3,4W


   DATA STREAM A296
        DELCO SDM E/SIR
        USAGE:
             1995      6E,K,Ksp


   DATA STREAM A297
       CCM USAGE:
                 1995 "Y" CAR WITH 5.7L (LT1) (VIN=P) AND  5.7L  (LT5) (VIN=J)

  DATA STREAM A298   not assigned
  DATA STREAM A299   not assigned

   DATA STREAM A300
        DELCO SDM AI/SIR
        USAGE:
             1995              1M


  DATA STREAM A201   not assigned
  DATA STREAM A202   not assigned
  DATA STREAM A203   not assigned
  DATA STREAM A204   not assigned
  DATA STREAM A205   not assigned
  DATA STREAM A206   not assigned
  DATA STREAM A207   not assigned
  DATA STREAM A208   not assigned


  DATA STREAM A309

       OBD-II   VCMX-A
       USAGE:   4.3L   L35  VIN=W    1995 S,T TRUCKS